## Slide 1: Process Metrics
Business 2710 – Class 7

## Slide 2: Capacity
Maximum output of a resource
Measured in units per time period
Example
    An assembler of an electric motor can do her task in 30 seconds
    Her capacity is 60 minutes per hour/0.5 minutes per unit = 120 unites per hour

## Slide 3: Throughput
Actual total volume of production through a facility (machine, department, factory, etc.)
Units per time period
Example
    A company process 120 sales orders per day

## Slide 4: Cycle Time
Time between completion of two discrete units/cases.
Example:
    Motors assembled at a rate of 120 per hour
    Cycle time = 30 seconds
Example:
    Sales order processed at a rate of 10 per business day
    Cycle time = 8/10 = 0.8 hours = 48 minutes

## Slide 5: Throughput Time
Length of time when case begins until completed
Example:
    Electric motors assembled on a line with 15 operators, each with a labor time of 30 seconds
    Throughput time = 7.5 minutes (15 x 0.5)
    Capacity = 120 motors per hour
    Cycle time = 30 seconds

## Slide 6: Throughput Time
Example:
    Sales orders processed using 10 steps, each with a time of 10 minutes
    Throughput time = 10 x 10 minutes = 100 minutes
    Capacity = 6 sales orders per hour
    Cycle time = 10 minutes

## Slide 7: Utilization
A measure of how intensively a resource is being used to produce a good or service
Compares actual time used to available time
Example:
    A worker who is busy 45 minutes per hour
    Utilization = 45/60 = 75%
Example:
    A worker capable of entering 10 sales order per day but enters only 8
    Utilization = 8/10 = 80%

## Slide 8: Lead Time
The time between initiation of an order and the receipt of goods
Includes
    Order preparation time
    Queuing/waiting time
    Processing time
    Move or transportation time
    Inspection time

## Slide 9: Setup Time
The length of time require to change a specific machine, resource, work center or line from making the last good piece of one type of product to the first good piece of another type of product
Costs associated with setup may include scrap costs, calibration costs, labor downtime costs, lost sales, etc.

## Slide 10: Other Process Metrics
Process cost (activity-based costing)
Process “value added,” e.g. revenue
Process variability (“six-sigma”)

## Slide 11: Example
“A Tale of Two Invoices”

## Slide 12: Example: Accounts Payable Process
The accounts payables process has four steps that are done by four different employees (resources) in sequence
    The mail clerk enters the invoice
    The AP specialist analyzes and codes the invoice
    The purchasing specialist sets up the vendor for the invoice
    The controller issues and signs a cheque for the invoice

## Slide 13: Example (continued)
Invoice entry takes 15 minutes
Analyzing and coding takes 20 minutes
Vendor setup takes 30 minutes
Issuing the cheque takes 20 minutes
Analyzing and coding invoices is highly specialized and can only be performed by the AP specialist.
On average, ProductIFF receives 15 invoices per 8 hour day

## Slide 14: Example (continued)
What is the capacity of the current process?
What is the maximum number of invoices that ProductIFF Inc. can process per day?
What is the average utilization of
    The mail clerk?
    The AP specialist?
    The purchasing specialist?
    The controller?

## Slide 15: Example (continued)
ProductIFF Inc. has suggested that the vendor for commonly purchased items must be set up before ordering, so that they are available when an invoice arrives. From experience, this would affect half of the invoices
    What is the capacity of this modified process?
ProductIFF Inc.’s business expands and there is an increase to 20 invoices per day
    What (if any) changes would be needed in the process to support this invoice rate of 20 invoices per day? Assume early vendor setup as above.

## Slide 16: Example (continued)
Resource | Number | Minutes per Order | Available minutes per day | Capacity of resources | % Utilization
Mail Clerk | 1 | 15 | 480 | 32 | 46.875
AP specialist | 1 | 20 | 480 | 24 | 62.500
Purchasing Specialist | 1 | 30 | 480 | 16 | 93.750
Controller | 1 | 20 | 480 | 24 | 62.500

## Slide 17: Example (continued)
Capacity = 16 invoices per day
    Vendor setup is the bottleneck
Throughput time for invoice = 15+20+30+20 = 85 min
Throughput = 15 invoices per day (unconstrained)
Average cycle time = 480 min per day / 15 invoices per day = 32 minutes
Utilization of resources (See table)